## Slide 1: Team :
ELGANG
Mini CNC Plotter Project
Tamer Medhat

## Slide 2: What is a CNC Plotter?
A CNC Plotter is a computer- controlled drawing machine that moves a pen or tool across a flat surface to draw images, text, or patterns with precision. The term CNC stands for Computer Numerical Control, meaning the machine follows programmed instructions (G-code) to move in the X, Y (and sometimes Z) directions. Mini CNC plotters are often built using 3D printers and are widely used in educational, prototyping, and artistic applications.

## Slide 3: Components Required
To build a Mini CNC plotter, you need both hardware and software components:
Hardware:
Arduino Uno:Main controller that sends signals to the motors based on the code received from the computerز
Stepper Motors (28BYJ-48)
Used to move the X and Y axes accurately in small steps.
ULN2003 Driver Boards
These control the stepper motors by receiving signals from the
Arduino.
Breadboard
Used to connect wires and distribute power without soldering.
Jumper Wires
•
•
•
Connect all the components together to send signals and power.
USB Cable
Connects the Arduino to the computer for power and data transfer.
Mechanical Frame
Holds all parts in place and provides a base for movement.
Pen Holder
Holds a pen to draw based on the CNC movements.
Software:
•
GRBL Firmware: Loaded onto the Arduino to interpret G-code.
Arduino IDE: Used to upload the GRBL firmware.
G-code Sender Software (like Universal G-code Sender): Sends drawing instructions to the machine.
Inkscape with G-code plugin: Used to design or convert images into G-code.

## Slide 4: Working Principle
The CNC plotter works on the basis of coordinate-based motion control:
A design is converted into G-code — a series of commands that represent movements.
The G-code is sent to the Arduino Uno running GRBL firmware.
The firmware translates these commands into electrical signals.
The CNC Shield and motor drivers translate the signals into stepper motor movements.
As the motors rotate, the pen moves across X and Y axes to draw the pattern.
The Z-axis (if implemented) lifts or drops the pen between drawing segments.

## Slide 5: Mechanical Assembly
Assembly Steps:
  Fix the Motors:
Attach the stepper motors firmly to the base/frame.
  Add Linear Rails or Sliders:
Install the sliding mechanism that allows
movement in X and Y directions.
  Connect Motion System:
Use belts, gears, or threaded rods to move the platform.
  Install the Pen Holder:
Place the pen mount in the middle so it can reach the drawing area.
Key Features of the Structure:
Stable & Precise:
The frame should be light but strong enough to keep the movements accurate.
Smooth Motion:
Use linear rails or sliders so the pen moves without
shaking or friction.
Recycled Components:
You can reuse parts from old CD/DVD drives (like motors and rails) to save cost.
Tool Mount (Pen Holder):
A simple holder for a pen, marker, or even a laser. You can lift it manually or use a servo motor.

## Slide 6: Electronics Setup
Connect Stepper Motors: Plug each motor into the correct slot on the CNC Shield using the motor drivers.
Mount CNC Shield:
Place the CNC Shield directly on
top of the Arduino Uno.
Upload GRBL Firmware:
Use the Arduino IDE to upload GRBL to the Arduino — this allows it to read G-code commands.
Set Jumpers:
Adjust the small jumper pins on the CNC Shield to control microstepping and motor current.
Connect Power Supply:
Give the CNC Shield power
(usually 12V) to run the motors.

## Slide 7: Software Used
GRBL (on
Arduino): Lightweight firmware that interprets G- code.
Arduino IDE: For firmware upload.
Universal G-code Sender (UGS): GUI-based tool to load and send G-code to the machine.
Inkscape: A vector graphics editor used to design shapes.
•.

## Slide 8: direction and steps.
Calibration & Testing
Test each motor for correct
Calibrate steps per millimeter in GRBL settings.
Ensure pen pressure and lift are
optimized.
Adjust the speed/feed rate to avoid skipping or distortion.
Print test shapes (square, circle, text) to check accuracy.

## Slide 9: Some pictures of the project :

## Slide 10: Some drawings:

## Slide 11
Simulation

## Slide 12: Applications:
Educational Projects: Teach robotics, electronics, and automation.
PCB Prototyping: Plot circuit layouts (with conductive ink).
Art and Design: Automated sketching and signature machines.
Laser Engraving (advanced mods): Replace pen with a low-power laser.
Small-scale manufacturing: Personalized labels, logos, or cards.

## Slide 13: Conclusion
The Mini CNC Plotter is a perfect example of how multiple disciplines — electronics, mechanics, and programming — come together in one project. It’s low-cost, educational, and flexible. Ideal for beginners and hobbyists looking to explore automation, control systems, and creative tech solutions.

## Slide 14: Thanks